## Slide 1
P V S Phaneendra
CircuitSutra Technologies Pvt. Ltd.
Aug 2011
Indirectly Associating Parameters SystemC CCI WG
Notes: <number>
<number>
<number>
<number>

## Slide 2
Objective of the present example is to demonstrate the following :
  Parameter Searches (R3), and
  Parameter Value Synchronization to address Different Names, Same Intended Meaning (UC9)
  value translation (e.g. units) is demonstrated between the associated parameters.
2
Indirectly Associating Parameters
Notes: <number>
<number>
<number>
<number>

## Slide 3
Top_Module
Create two parameter_owner modules
Get the handles of the of the owner modules’ parameters with the configuration broker using Name-based Look Up Access
Parameter_Configurator
Param_Name : clk_freq_Hz
Default Value : 1 (Hz)
Instance#1 Parameter_Owner
Param_Name : clock_speed_KHz
Default Value : 2 (KHz)
Instance#2 Parameter_Owner
Instantiate a param_value_sync_with_cf class to synchronize the parameter values
Sends the list of selected cci_param_handles to the param_value_sync_with_cf class
3
Example Illustration
Notes: <number>
<number>
<number>
<number>

## Slide 4
param_value_sync_with_cf
Top_Module
Configurator already stored parameter handles
Parameter_Configurator
Param_Name : clk_freq_Hz
Default Value : 1 (Hz)
Instance#1 Parameter_Owner
Param_Name : clock_speed_KHz
Default Value : 2 (KHz)
Instance#2 Parameter_Owner
Select a list of parameters using the get_param_handle API (Name-based Look Up Access) and pass it to the param_value_sync_cf
With one cci-parameter as the reference, write it’s default value
to the other cci-parameter using set_cci_value
A way to sync the startup values of the parameters
4
Example Illustration Contd.
Notes: <number>
<number>
<number>
<number>

## Slide 5
Top_Module
Param_Name : clk_freq_Hz
Default Value : 1 (Hz)
Instance#1 Parameter_Owner
Param_Name : clock_speed_KHz
Default Value : 2 (KHz)
Instance#2 Parameter_Owner
Register ‘post_write’ callbacks on the selected parameters clk_freq_Hz and clock_speed_KHz
Synchronize the values of parameter of the two owners (before BEOE phase begins) synchValuesWithCF(cci::cci_param_handle _param_handle_1, cci::cci_param_handle _param_handle_2, double conversion_factor)
param_value_sync_with_cf
New Value : 0.001 (KHz)
5
Example Illustration Contd.
Parameter_Configurator
Configurator already stored handles of the parameters
Notes: <number>
<number>
<number>
<number>

## Slide 6
Top_Module
Param_Name : clk_freq_Hz
Default Value : 1 (Hz)
Instance#1 Parameter_Owner
Param_Name : clock_speed_KHz
Default Value : 2 (KHz)
Instance#2 Parameter_Owner
param_value_sync_with_cf
Old Value : 0.001 (KHz)
Parameter_Configurator
Within BEOE phase, change value of clk_freq_Hz via CONFIGURATOR to 5000 (Hz)
New Value : 5000 (Hz)
New Value : 5 (KHz)
Registered Callback for clk_freq_Hz parameter is called and clock_speed_KHz value is synchronized with the clk_freq_Hz value
6
Example Illustration Contd.
Notes: <number>
<number>
<number>
<number>

## Slide 7
Top_Module
Param_Name : clk_freq_Hz
Default Value : 1 (Hz)
Instance#1 Parameter_Owner
Param_Name : clock_speed_KHz
Default Value : 2 (KHz)
Instance#2 Parameter_Owner
param_value_sync_with_cf
Old Value : 5 (KHz)
Old Value : 5000 (Hz)
Parameter_Configurator
At 0ns, change value of clck_speed_KHz via CONFIGURATOR to 12 (KHz)
Simulation starts
New Value : 12 (KHz)
Registered Callback for clock_speed_KHz parameter is called and clk_freq_Hz value is synchronized with the clock_speed_KHz value
New Value : 12000 (Hz)
7
Example Illustration Contd.
Notes: <number>
<number>
<number>
<number>

## Slide 8: Expected Output (ex12_Indirectly_Associateing_Parameters.log)
SystemC Simulation
Info: top_mod.param_owner1: @0 s, [OWNER C_TOR] : Parameter Name : top_mod.param_owner1.clk_freq_Hz, Value : 1
Info: top_mod.param_owner2: @0 s, [OWNER C_TOR] : Parameter Name : top_mod.param_owner2.clock_speed_KHz, Value : 2
Info: top_mod: @0 s, [TOP_MODULE C_TOR] : Parameter Name : top_mod.param_owner1.clk_freq_Hz, Value : 1.0
Info: top_mod: @0 s, [TOP_MODULE C_TOR] : Parameter Name : top_mod.param_owner2.clock_speed_KHz, Value : 2.0
Info: top_mod.param_value_sync_with_cf: @0 s, Parameter1_str: top_mod.param_owner1.clk_freq_Hz
Info: top_mod.param_value_sync_with_cf: @0 s, Parameter2_str : top_mod.param_owner2.clock_speed_KHz
Info: top_mod.param_value_sync_with_cf: @0 s, ConversionFactor : 0.001
Info: param_cfgr: @0 s, [CFGR C_TOR] : Parameter Name : top_mod.param_owner1.clk_freq_Hz, Value : 1.0
Info: param_cfgr: @0 s, [CFGR C_TOR] : Parameter Name : top_mod.param_owner2.clock_speed_KHz, Value : 0.001
Info: sc_main: Begin Simulation.
Info: param_cfgr: @0 s, [CFGR within beoe] Within the BEOE phase
Info: param_cfgr: @0 s, [CFGR within beoe] : Changing the 'clk_freq_Hz' of OWNER (1) to 5000 (Hz).
Notes: <number>

## Slide 9: Contd.
Info: top_mod.param_value_sync_with_cf: @0 s, [PARAM_VALUE_SYNC - post_write callback] : Parameter Name : top_mod.param_owner1.clk_freq_Hz, Value : 5000.0
Info: top_mod.param_value_sync_with_cf: @0 s, [PARAM_VALUE_SYNC - post_write callback] : Parameter Name : top_mod.param_owner2.clock_speed_KHz, Value : 5.0
Info: param_cfgr: @0 s, [CFGR within beoe] : Parameter Name : top_mod.param_owner1.clk_freq_Hz, Value : 5000.0
Info: param_cfgr: @0 s, [CFGR within beoe] : Parameter Name : top_mod.param_owner2.clock_speed_KHz, Value : 5.0
Info: param_cfgr: @0 s, @ 0 s
Info: param_cfgr: @0 s, [CFGR] : Changing the 'clock_speed_KHz' of OWNER (2) to 12 (KHz).
Info: top_mod.param_value_sync_with_cf: @0 s, [PARAM_VALUE_SYNC - post_write callback] : Parameter Name : top_mod.param_owner2.clock_speed_KHz, Value : 12.0
Info: top_mod.param_value_sync_with_cf: @0 s, [PARAM_VALUE_SYNC - post_write callback] : Parameter Name : top_mod.param_owner1.clk_freq_Hz, Value : 12000.0
Info: param_cfgr: @0 s, [CFGR] : Parameter Name : top_mod.param_owner1.clk_freq_Hz, Value : 12000.0
Info: param_cfgr: @0 s, [CFGR] : Parameter Name : top_mod.param_owner2.clock_speed_KHz, Value : 12.0
Info: sc_main: End Simulation.
Notes: <number>