## Slide 1
Hiding Parameters SystemC CCI WG
P V S Phaneendra
CircuitSutra Technologies Pvt. Ltd.
Sep 2011
Notes: <number>
<number>
<number>
<number>

## Slide 2
Hiding Parameters
Objective of the present example is to demonstrate the following :
  Constructing and activating a private broker to restrict access to the parameters
This example also exhibits the ability to manage complex interdependencies as described in Parameter Hiding (UC13)
2
Notes: <number>
<number>
<number>
<number>

## Slide 3: Example Explanation
A small subsystem (parent and child module) are wrapped within a module (ex14_private) to control visibility of the contained parameters
The wrapper makes it easy to:
  Establish scope of the private broker as the entire subsystem
  Identify exceptions (parameters to be exposed) prior to construction of any subsystem parameters
Note: the subsystem doesn’t need to be modified itself to make this happen

## Slide 4
wrapper
configurator
Top module
Example Illustration (Contd.. 1)
Initialize handle to parent_int_buffer parameter of the PARENT
Instantiate the child module : child_inst(“child_inst”)
Constructs parameters as shown below: parent_int_param(“parent_int_param”, 300);
parent_buffer(“parent_int_buffer”, 350);
cci::cci_param<int> priv_int_param with a DEFAULT VALUE of 100
cci::cci_param<int> pub_int_param with a DEFAULT VALUE of 150
4
child
Initialize and register a private broker of type cci_utils::broker (pbroker)
Identify in advance the parameters to be exposed pbroker.expose.insert("Top.private.parent_inst.parent_int_buffer"); pbroker.expose.insert("Top.private.parent_inst.child_inst.pub_int_param");
Then instantiate the parent module m_parent_inst = new ex14_parent(“parent_inst”);
parent
Notes: <number>
<number>
<number>
<number>

## Slide 5
Top module
parent
child
Example Illustration (Contd.. 2)
POST_WRITE callback implemented on parameter parent_buffer so that when a change occurs on the parent_buffer of the parent module, the same will be reflected on to the priv_int_param of the child module
NOTE: In this case, only parent_buffer of PARENT module and pub_int_param of CHILD module can write to the priv_int_param of the child module directly
configurator
Stores param handle of parent_int_buffer (publicly visible)
priv_int_param
Infrastructure implemented within the model for making necessary value changes to the private parameter of ‘child’
pub_int_param
5
Notes: <number>
<number>
<number>
<number>

## Slide 6
Top module
Example Illustration (Contd.. 3)
configurator
Get visible parameters list using m_broker.get_param_handles(); where, m_broker(cci::cci_broker_manager::get_broker());
parent
Get visible parameters list using m_broker.get_param_handles(); where, m_broker(cci::cci_broker_manager::get_broker())
child
Get visible parameters list using m_broker.get_param_handles(); where, m_broker(cci::cci_broker_manager::get_broker())
Demonstrating Parameter Hiding
Top.private.parent_inst.child_inst.priv_int_param Top.private.parent_inst.parent_int_param
Top.private.parent_inst.child_inst.pub_int_param
Top.private.parent_inst.parent_int_buffer
Top.private.parent_inst.child_inst.priv_int_paramTop.private.parent_inst.parent_int_param Top.private.parent_inst.child_inst.pub_int_param
Top.private.parent_inst.parent_int_buffer
Top.parent_inst.child_inst.pub_int_param
Top.parent_inst.parent_int_buffer
6
Notes: <number>
<number>
<number>
<number>

## Slide 7
Top module
parent
Default Value : 300
Parameter Name : parent_int_param
Parameter Name : parent_int_buffer
Default Value : 350
Example Illustration (Contd.. 4)
Illustrating the flow when a valid value change is to be done to a private parameter (Implemented via callbacks)
configurator
Write new value 1000 to the parent_int_buffer using set_cci_value(…) parent_param_handle.set_cci_value(cci::cci_value(1000));
child
New Value : 1000
Parameter Name : priv_int_param
Default Value : 100
Parameter Name : pub_int_param
Default Value : 150
New Value : 1000
7
Notes: <number>
<number>
<number>
<number>

## Slide 8: Expected Output (ex14_Hiding_Parameters.log)
SystemC Simulation
Info: Top.private.parent_inst.child_inst: @0 s, [CHILD C_TOR] : Is Private Broker? : true
Info: Top.private.parent_inst.child_inst: @0 s, [CHILD C_TOR] : Parameter Name : Top.private.parent_inst.child_inst.priv_int_param Parameter Value : 100
Info: Top.private.parent_inst.child_inst: @0 s, [CHILD C_TOR] : Parameter Name : Top.private.parent_inst.child_inst.pub_int_param Parameter Value : 150
Info: Top.private.parent_inst: @0 s, [PARENT C_TOR] : Parameter Name : Top.private.parent_inst.parent_int_param Parameter Value : 300
Info: Top.private.parent_inst: @0 s, [PARENT C_TOR] : Parameter Name : Top.private.parent_inst.parent_int_buffer Parameter Value : 350
Info: sc_main: Begin Simulation.
Info: Top.param_cfgr: @0 s, [CFGR] : Parameter Name : Top.private.parent_inst.parent_int_buffer Parameter Value : 350
Info: Top.private.parent_inst.child_inst: @0 s, @ 0 s Visible parameters to 'child' module
Info: Top.private.parent_inst.child_inst: @0 s, [CHILD] : Parameter Name : Top.private.parent_inst.child_inst.priv_int_param
Info: Top.private.parent_inst.child_inst: @0 s, [CHILD] : Parameter Name : Top.private.parent_inst.parent_int_param
Notes: <number>

## Slide 9: Contd.
Info: Top.private.parent_inst.child_inst: @0 s, [CHILD] : Parameter Name : Top.private.parent_inst.child_inst.pub_int_param
Info: Top.private.parent_inst.child_inst: @0 s, [CHILD] : Parameter Name : Top.private.parent_inst.parent_int_buffer
Info: Top.private.parent_inst: @5 ns, @ 5 ns Visible parameters to the 'parent' module
Info: Top.private.parent_inst: @5 ns, [PARENT] : Parameter Name : Top.private.parent_inst.child_inst.priv_int_param
Info: Top.private.parent_inst: @5 ns, [PARENT] : Parameter Name : Top.private.parent_inst.parent_int_param
Info: Top.private.parent_inst: @5 ns, [PARENT] : Parameter Name : Top.private.parent_inst.child_inst.pub_int_param
Info: Top.private.parent_inst: @5 ns, [PARENT] : Parameter Name : Top.private.parent_inst.parent_int_buffer
Info: Top.param_cfgr: @15 ns, @ 15 ns Visible parameters to the 'configurator' module
Info: Top.param_cfgr: @15 ns, [CFGR] : Parameter Name : Top.private.parent_inst.child_inst.pub_int_param
Info: Top.param_cfgr: @15 ns, [CFGR] : Parameter Name : Top.private.parent_inst.parent_int_buffer
Info: Top.param_cfgr: @20 ns, @ 20 ns
Notes: <number>

## Slide 10: Contd.
Info: Top.param_cfgr: @20 ns, [CFGR] : Change the value of the 'parent_int_buffer' to '1000'
Info: Top.private.parent_inst: @20 ns, [PARENT - post_write_cb] : Parameter Name : Top.private.parent_inst.parent_int_buffer Parameter Value : 1000
Info: Top.param_cfgr: @20 ns, [CFGR] : Parameter Name : Top.private.parent_inst.parent_int_buffer Parameter Value : 1000
Info: Top.private.parent_inst.child_inst: @25 ns, @ 25 ns
Info: Top.private.parent_inst.child_inst: @25 ns, [CHILD] : Parameter Name : Top.private.parent_inst.child_inst.priv_int_param Parameter Value : 1000
Info: sc_main: End Simulation.
Notes: <number>