## Slide 1
User Defined Data Type
SystemC CCI WG
Girish Verma, P V S Phaneendra
CircuitSutra Technologies Pvt. Ltd.
Sep 2011
Notes: <number>
<number>

## Slide 2
<number>
Objective of the present example is to demonstrate the following :
  Adding support for user-defined data types, including complex structures
  Show access using both JSON values and cci_value
2
User Defined Data Types
Notes: <number>
<number>
<number>
<number>
<number>

## Slide 3
<number>
User Defined Data Types
sc_main()
Observer
(A simple C++ class, not an SC_MODULE)
Parameter_Owner
Parameter_Configurator
Instantiates user-defined data type cci-parameter
Note#1 : For a detailed understanding of registration and implementation of callbacks, please go through the presentation for ex#8 or ex#11 and ex#12
Registers different types of callbacks (pre_read, pre_write & post_write) on the parameters of interest to monitor their activities
Note#2 : The originator information will be displayed by the shape on the right
Reporter : Observer
Callback Type : cb_type
Originator : originator_name
Includes the user_datatype.h
3
Within the Callbacks implementation : Name of the originator : ev.originator.name();
Notes: <number>
<number>

## Slide 4
<number>
Step#1 : Defining a User-Defined Data Type
Declare a C++ class/structure for the user-defined data type (see the following slide)
Create a default constructor for the user-defined data type structure
Also provide an overloaded constructor that is useful to assign the user-defined values in the desired manner
Implement cci_value_converter<user-defined-type> with pack and unpack functions (not shown – see example code)
Overload the insertion (<<) operator to provide convenience in reporting
4
User Defined Data Types
Notes: <number>
<number>

## Slide 5
<number>
Infrastructure to be created : Creating Data Structure
struct route_table_ut
{
/// Default Constructor
route_table_ut()
: s_address(0x0) //Source Address
, d_address(0x0) //Destination Address
, index(0x0) //Index
{
// Nothing to implement
}
/// Overloaded Constructor
route_table_ut(int saddr, int daddr, int idx)
: s_address(saddr)
, d_address(daddr)
, index(idx)
{
// Nothing to implement
}
int s_address; // Slave Address
int d_address; // Destination Address
int index; // Index
};// End of STRUCT
5
User Defined Data Types
Notes: <number>
<number>

## Slide 6
<number>
Overloading insertion operator of C++
std::ostream& operator <<(std::ostream& os, const route_table_ut& ud)
{
cci::cci_value udv(ud);
return os << udv;
}
6
User Defined Data Types
Notes: <number>
<number>

## Slide 7
<number>
Parameter Configurator
Parameter Owner
Before the instantiation of the modules
Get handle to the DEFAULT BROKER using the above Originator
cci::cci_broker_handle globalBroker = cci::cci_broker_manager::get_broker(myOriginator);
sc_main()
Instantiate a cci_originator instance to get access to the DEFAULT BROKER
cci::cci_originator myOriginator(“sc_main_originator”);
Set preset value using set_preset_value API
std::string init_str("{\"s_address\":256,\"d_address\":512,\"index\":0}");
globalBroker.set_preset_cci_value(“param_owner.User_data_type_param”, cci::cci_value::from_json(init_str));
Create instances of the modules now
parameter_owner param_owner(“param_owner”);
parameter_configurer param_cfgr(“param_cfgr); observer observer_obj;
8
User Defined Data Types
Notes: <number>
<number>

## Slide 8
<number>
Parameter Configurator
Parameter Owner
Set name and assign default value :
udt_param("User_data_type_param",route_table_ut(0x200,0x300,1)
Prior to 0ns
Query parameter’s Default Value using get_default_value() API:
udt_param.get_default_value();
Returns Value = {"s_address":512,"d_address":768,"index":1}
Set documentation :
const std::string init_desc = “This is user-defined data type”;
udt_param.set_description(init_desc);
Declare handle for the parameter
cci::cci_param_handle udt_param_handle;
cci::cci_param<route_table_ut> udt_param;
Query parameter name :
udt_param.name();
Returns Name : param_owner.User_data_type_param
Query parameter’s Value using get() API:
udt_param.get();
Returns Value = {"s_address":256,"d_address":512,"index":0}
9
User Defined Data Types
Notes: <number>
<number>

## Slide 9
<number>
Parameter Configurator
Parameter Owner
Query parameter’s documentation :
udt_param.get_description();
Returns Documentation : This is user-defined data type
Set new value :
udt_param.set_cci_value("{\"s_address\":768,\"d_address\":1024,\"index\":2}");
Reporter : Observer
Callback Type : pre_write, post_write
Originator : owning_param
@ 0ns
@ 2ns
Query the present value :
udt_param.get_value();
Returns Value = {"s_address":768,"d_address":1024,"index":2}
Reporter : Observer
Callback Type : pre_read
Originator : owning_param
10
User Defined Data Types
Notes: <number>
<number>

## Slide 10
<number>
Parameter Configurator
Parameter Owner
Query Name : udt_param_handle.name();
Returns value = param_owner.User_data_type_param
@ 4ns
Query Value : udt_param_handle.get_cci_value();
Returns Value : {"s_address":768,"d_address":1024,"index":2}
Query Documentation : udt_param_handle.get_description();
Returns Value : This is user-defined data type
Reporter : Observer
Callback Type : pre_read
Originator : param_cfgr
@ 6ns
Set New Value :
std::string set_string "{\"s_address\":1024,\"d_address\":1280,\"index\":3}"); udt_param_handle.set_cci_value(cci::cci_value::from_json(set_string));
Reporter : Observer
Callback Type : pre_write, post_write
Originator : param_cfgr
11
User Defined Data Types
Notes: <number>
<number>

## Slide 11
<number>
Parameter Configurator
Parameter Owner
@ 8ns
Query Name : udt_param_handle.name();
Returns value = param_owner.User_data_type_param
Query Value : udt_param_handle.get_cci_value();
Returns Value : {"s_address":1024,"d_address":1280,"index":3}
Reporter : Observer
Callback Type : pre_read
Originator : param_cfgr
12
User Defined Data Types
Notes: <number>
<number>

## Slide 12: Expected Output (ex16_User_Defined_Data_Type.log)
SystemC Simulation
Info: sc_main: [MAIN] : Setting preset value 's_address:256,d_address:512,index:0' to UDT
Info: param_owner: @0 s, Prior to 0 s demonstrating 'get_default_value()'
Info: param_owner: @0 s, [OWNER -> Retrieve] : Parameter name : param_owner.User_data_type_param
Info: param_owner: @0 s, [OWNER -> Retrieve] : Using 'get_default_value()' : {"s_address":512,"d_address":768,"index":1}
Info: param_owner: @0 s, [OWNER -> Retrieve] : Parameter Value' : {"s_address":256,"d_address":512,"index":0}
Info: param_owner: @0 s, [OWNER -> Set] : Param desc - 'This is user-defined data type
Info: param_cfgr: @0 s, [CFGR C_TOR] : Broker Type : DEFAULT_BROKER - is not a private broker.
[OBSERVER C_TOR] : Broker Type : DEFAULT_BROKER - is not a private broker.
Info: sc_main: Begin Simulation.
Info: param_owner: @0 s, @ 0 s
Info: param_owner: @0 s, [OWNER -> Retrieve] : Description : This is user-defined data type
Info: param_owner: @0 s, [OWNER -> Set] : New Value param_owner.User_data_type_param 's_address:768,d_address:1024,index:2'
[OBSERVER pre_write_cb] : Parameter Name : param_owner.User_data_type_param Originator info : param_owner
Notes: <number>

## Slide 13: Contd.
[OBSERVER post_write_cb] : Parameter Name : param_owner.User_data_type_param Originator info : param_owner
Info: param_owner: @2 ns, @ 2 ns
[OBSERVER pre_read_cb] : Parameter Name : param_owner.User_data_type_param Originator info : param_owner
[OBSERVER post_read_cb]: Parameter Name : param_owner.User_data_type_param Originator info : param_owner
Info: param_owner: @2 ns, [OWNER -> Retrieve] : UDT Value : {"s_address":768,"d_address":1024,"index":2}
Info: param_cfgr: @4 ns, @ 4 ns
Info: param_cfgr: @4 ns, [CFGR -> Retrieve] : Parameter name : param_owner.User_data_type_param
[OBSERVER pre_read_cb] : Parameter Name : param_owner.User_data_type_param Originator info : param_cfgr
[OBSERVER post_read_cb]: Parameter Name : param_owner.User_data_type_param Originator info : param_cfgr
Info: param_cfgr: @4 ns, [CFGR -> Retrieve] : Parameter value: {"s_address":768,"d_address":1024,"index":2}
Info: param_cfgr: @4 ns, [CFGR -> Retrieve] : Parameter desc: This is user-defined data type
Notes: <number>

## Slide 14: Contd.
Info: param_cfgr: @6 ns, @ 6 ns
Info: param_cfgr: @6 ns, [CFGR -> Set] : Value - 's_address:1024,d_address:1280,index:3
[OBSERVER pre_write_cb] : Parameter Name : param_owner.User_data_type_param Originator info : param_cfgr
[OBSERVER post_write_cb] : Parameter Name : param_owner.User_data_type_param Originator info : param_cfgr
Info: param_cfgr: @8 ns, @ 8 ns
Info: param_cfgr: @8 ns, [CFGR -> Retrieve] : Parameter name : param_owner.User_data_type_param
[OBSERVER pre_read_cb] : Parameter Name : param_owner.User_data_type_param Originator info : param_cfgr
[OBSERVER post_read_cb]: Parameter Name : param_owner.User_data_type_param Originator info : param_cfgr
Info: param_cfgr: @8 ns, [CFGR -> Retrieve] : Parameter value: {"s_address":1024,"d_address":1280,"index":3}
Info: sc_main: End Simulation.
Notes: <number>