## Slide 1
P V S Phaneendra
CircuitSutra Technologies Pvt. Ltd.
May 2011
Parameter Value Locking SystemC CCI WG
Notes: <number>
<number>
<number>

## Slide 2
The objectives of this example are to demonstrate the following:
    locking and unlocking parameter values
    reporting the rejection of an attempt to modify a locked parameter’s value
Note: locking and unlocking is shown a context different than for structural parameters, already shown in Example 3.
2
Parameter Value Locking
Notes: <number>
<number>
<number>

## Slide 3
Attribute | Indicator
Returned Status True | 
Returned Status False | 
Information: Info | 
Warning | 
Exception Thrown : Error | 
Kindly note that the above legend has not been used to demonstrate locked() API's (used for querying a CCI parameter's locking status) status.
Usage : int_param_handle.locked()
“locked()” API returns TRUE when a parameter is in locked state and FALSE when in unlocked state
3
Legend Diagram
Notes: <number>
<number>
<number>

## Slide 4
Set parameter value to 1
int_param = 1;
int_param.locked()
int_param.locked()
int_param.locked()
/Accellera/CCI/SET_PARAM_FAILED: Parameter locked.
NOTE : Used TRY-CATCH mechanism to catch the error
Within Constructor Default value : 0
Within Constructor
Assign the int_param_handle from broker
Parameter_Onwer
Parameter_Configurator
Lock without password
int_param.lock();
Parameter Locking Status: 1 Parameter Value : 0
Parameter Locking Status: 0 Parameter Value : 0
@ 0 ns
Parameter Locking Status: 1 Parameter Value : 0
Parameter Locking Status: 1 Parameter Value : 0
4
Parameter Value Locking Sequence Diagram
Notes: <number>
<number>

## Slide 5
int_param.is_locked()
int_param_handle.is_locked()
Unlock parameter without password
int_param.unlock();
Parameter_Onwer
Parameter_Configurator
Check if locked and if unlocked, only then assign value to '2'
Result = Locked! Hence, Value can't be assigned
@ 2 ns
Parameter Locking Status: 1 Parameter Value : 0
Parameter Locking Status: 1 Parameter Value : 0
Parameter has to be unlocked by the OWNER (the module that locked it)
@ 5 ns
int_param_handle.is_locked()
Set parameter value to 3
int_param_handle.
set_cci_value(
cci::cci_value(3));
Parameter Locking Status: 0 Parameter Value : 3
@ 7 ns
5
Parameter Value Locking Sequence Diagram
Contd.
Notes: <number>
<number>

## Slide 6
int_param_handle.is_locked()
Parameter_Onwer
Parameter_Configurator
Lock parameter without password
int_param_handle.lock();
Parameter Locking Status: 1 Parameter Value : 3
int_param_handle.is_locked()
Unlock parameter without password
int_param_handle.unlock();
Parameter Locking Status: 0 Parameter Value : 3
int_param_handle.is_locked()
Lock parameter with password
void* psswd = NULL;
int_param_handle.lock(&psswd);
Parameter Locking Status: 1 Parameter Value : 3
Parameter can’t be updated without the password ”&psswd” now
6
Parameter Value Locking Sequence Diagram
Contd.
Notes: <number>
<number>

## Slide 7
Parameter_Onwer
Parameter_Configurator
int_param_handle.is_locked()
Error: /Accellera/CCI/SET_PARAM_FAILED: Parameter locked.
Parameter Locking Status: 1 Parameter Value : 3
Check if locked and if unlocked, only then assign value to '4'
Result = Locked! Hence, Value can't be assigned
Parameter can’t be updated without the password ”&psswd”
int_param_handle.is_locked()
Unlock parameter with correct password
int_param_handle.unlock(&psswd);
Parameter Locking Status: 0 Parameter Value : 3
7
Parameter Value Locking Sequence Diagram
Contd.
Notes: <number>
<number>

## Slide 8
Parameter_Onwer
Parameter_Configurator
int_param.locked()
int_param.locked()
@ 10 ns
Lock parameter with password void* key = NULL;
int_param.lock(&key);
Parameter Locking Status: 1 Parameter Value : 3
Override parameter value to 4 without unlocking int_param.set(4, &key);
Parameter Locking Status: 1 Parameter Value : 4
8
Parameter Value Locking Sequence Diagram
Contd.
Notes: <number>
<number>

## Slide 9: Expected Output (ex13_Parameter_Locking.log)
SystemC Simulation
Info: param_owner: @0 s, [OWNER C_TOR] : Parameter locking status : 0 Value : 0
Info: sc_main: Begin Simulation.
Info: param_owner: @0 s, @ 0 s
Info: param_owner: @0 s, [OWNER] : Locking the parameter without password
Info: param_owner: @0 s, [OWNER] : Parameter locking status : 1 Value : 0
Info: param_owner: @0 s, [OWNER] : Try to set parameter value to 1 from 0
Info: param_owner: @0 s, [OWNER] : param_owner Failed to set parameter value to 1 from 0.
Info: param_owner: @0 s, [OWNER] : Caught Exception : Error: /Accellera/CCI/SET_PARAM_FAILED: Parameter locked.
In file: <removed by verify.pl>
In process: param_owner.run_owner @ 0 s
Info: param_owner: @0 s, [OWNER] : Parameter locking status : 1 Value : 0
Info: param_cfgr: @2 ns, @ 2 ns
Info: param_cfgr: @2 ns, [CFGR] : Parameter locking status : 1 Value : 0
Info: param_cfgr: @2 ns, [CFGR] : Cannot assign new value to the parameter as it is already locked!!
Notes: <number>

## Slide 10: Contd.
Info: param_cfgr: @2 ns, [CFGR] : Parameter locking status : 1 Value : 0
Info: param_owner: @5 ns, @ 5 ns
Info: param_owner: @5 ns, [OWNER] : Unlocking parameter (locked earlier) without password
Info: param_owner: @5 ns, [OWNER] : Parameter locking status : 0 Value : 0
Info: param_cfgr: @7 ns, @ 7 ns
Info: param_cfgr: @7 ns, [CFGR] : Parameter locking status : 0 Value : 0
Info: param_cfgr: @7 ns, [CFGR] : Parameter is not locked!! Assign a new value '3' to it
Info: param_cfgr: @7 ns, [CFGR] : Parameter locking status : 0 Value : 3
Info: param_cfgr: @7 ns, [CFGR] : Lock parameter without password
Info: param_cfgr: @7 ns, [CFGR] : Parameter locking status : 1 Value : 3
Info: param_cfgr: @7 ns, [CFGR] : Unlock parameter without password
Info: param_cfgr: @7 ns, [CFGR] : Parameter locking status : 0 Value : 3
Info: param_cfgr: @7 ns, [CFGR] : Lock with password
Info: param_cfgr: @7 ns, [CFGR] : Parameter locked with password (password not known to OWNER)
Info: param_cfgr: @7 ns, [CFGR] : Parameter locking status : 1 Value : 3
Info: param_cfgr: @7 ns, [CFGR] : Set parameter value to '4'
Notes: <number>

## Slide 11: Contd.
Info: param_cfgr: @7 ns, [CFGR] : Caught Exception : Error: /Accellera/CCI/SET_PARAM_FAILED: Parameter locked.
In file: <removed by verify.pl>
In process: param_cfgr.run_mutable_cfgr @ 7 ns
Info: param_cfgr: @7 ns, [CFGR] : Parameter locking status : 1 Value : 3
Info: param_cfgr: @7 ns, [CFGR] : Now, unlock with the correct password
Info: param_cfgr: @7 ns, [CFGR] : Parameter locking status : 0 Value : 3
Info: param_owner: @10 ns, @ 10 ns
Info: param_owner: @10 ns, [OWNER] : Parameter locking status : 0 Value : 3
Info: param_owner: @10 ns, [OWNER] : Directly lock the unlocked parameter with password
Info: param_owner: @10 ns, [OWNER] : Parameter locking status : 1 Value : 3
Info: param_owner: @10 ns, [OWNER] : Overwrite value of the (locked!) parameter to 4 without unlocking
Info: param_owner: @10 ns, [OWNER] : Parameter locking status : 1 Value : 4
Info: sc_main: End Simulation.
Notes: <number>