## Slide 1: Inter Parameter Value Constraints SystemC CCI WG
P V S Phaneendra
CircuitSutra Technologies Pvt. Ltd.
Aug 2011
Notes: <number>

## Slide 2
Inter_Parameter_Value_Constraints
Objective of the present example is to demonstrate the following :
  Establishing and maintaining inter-parameter value constraints (R16)
  Reporting inter-parameter value constraint violations
  The dynamic ability to reject values have been explained and contrasted to (static) locking
2
Notes: <number>
<number>
<number>
<number>

## Slide 3
‘X’ < 2n – 1 where, X : Memory Block Size, and n : Number of address Lines
Condition to be tested
3
Example Illustration
Notes: <number>
<number>
<number>
<number>

## Slide 4
processor
address_lines_register
Parameter Name : curr_addr_lines
Default Value : 9
memory_block
Parameter Name : mem_size
Default Value : 500
Get and store the handles for interrelated parameters of
address_lines_register and memory_block modules
Configurator
Defines a function that checks the condition : X < 2n-1 void TestCondition( int <addr_lines>, int <memory_size> ) function generates log whether or not the condition specifed is met
4
Example Illustration (Contd.. 1)
Notes: <number>
<number>
<number>
<number>

## Slide 5
processor
Get and store the handles for interrelated parameters of
address_lines_register and memory_block modules
Configurator
address_lines_register
Parameter Name : curr_addr_lines
Default Value : 9
memory_block
Parameter Name : mem_size
Default Value : 500
Infrastructure
Processor module registers POST_WRITE callbacks on base parameters of the child modules
Within callbacks implemention, the current values of the cci-parameters are fed to the TestCondition function
5
Example Illustration (Contd.. 2)
Notes: <number>
<number>
<number>
<number>

## Slide 6
processor
address_lines_register
Parameter Name : curr_addr_lines
Default Value : 9
memory_block
Parameter Name : mem_size
Default Value : 500
Get and store the handles for interrelated parameters of
address_lines_register and memory_block modules
Configurator
TestCondition function reports User may proceed with the present configuration
6
Example Illustration (Contd.. 3)
Notes: <number>
<number>
<number>
<number>

## Slide 7
processor
address_lines_register
Parameter Name : curr_addr_lines
Default Value : 9
memory_block
Parameter Name : mem_size
Default Value : 500
TestCondition function reports The address lines CANNOT address the current memory size
At 0ns, updates mem_size cci-parameter value to 640
Configurator
New Value : 640
7
Example Illustration (Contd.. 4)
Notes: <number>
<number>
<number>
<number>

## Slide 8
processor
address_lines_register
Parameter Name : curr_addr_lines
Default Value : 9
memory_block
Parameter Name : mem_size
Default Value : 500
Old Value : 640
TestCondition function reports The address lines CAN NOW address the current memory size
At 5ns, updates curr_addr_lines cci-parameter value to 10
Configurator
New Value : 10
8
Example Illustration (Contd.. 5)
Notes: <number>
<number>
<number>
<number>

## Slide 9
processor
address_lines_register
Parameter Name : curr_addr_lines
Default Value : 9
memory_block
Parameter Name : mem_size
Default Value : 500
Old Value : 640
TestCondition function reports User may proceed with the present configuration
At 10ns, updates mem_size cci-parameter value to 800
Configurator
New Value : 800
Old Value : 10
9
Example Illustration (Contd.. 6)
Notes: <number>
<number>
<number>
<number>

## Slide 10: Expected Output (ex05_Inter_Parameter_Value_Constraint.log)
SystemC Simulation
Info: sc_main: [MAIN] : In this example, the following is condition is verified
Info: sc_main: [MAIN] : x <= 2^n - 1
Info: sc_main: [MAIN] : where, 'x' : value of 'mem_block_size' (Memory Block size), and
Info: sc_main: [MAIN] : 'n' : total number of address lines - 'curr_addr_lines'
Info: processor.addr_lines_mod: @0 s, [ADDR_LINES_REG C_TOR] : Default Address Lines : 9
Info: processor.memory_block: @0 s, [MEMORY_BLOCK C_TOR] : Default Memory Size : 500
Info: processor: @0 s, [PROCESSOR fn] : User may proceed with the present configuration
Info: sc_main: Begin Simulation.
Info: param_cfgr: @0 s, @ 0 s
Info: param_cfgr: @0 s, [CFGR] : Changing the 'mem_size' to 640
Info: processor: @0 s, [PROCESSOR mem_block_post_wr_cb] : Parameter Name : processor.memory_block.mem_size Parameter Value : 640
Info: processor: @0 s, [PROCESSOR mem_block_post_wr_cb] : Parameter Name : processor.addr_lines_mod.curr_addr_lines Parameter Value : 9
Info: processor: @0 s, [PROCESSOR fn] : The address lines cannot address the current memory size
Notes: <number>

## Slide 11: Contd.
Info: param_cfgr: @5 ns, @ 5 ns
Info: param_cfgr: @5 ns, [CFGR] : Modify the 'curr_addr_lines' to 10
Info: processor: @5 ns, [PROCESSOR addr_lines_post_wr_cb] : Parameter Name : processor.addr_lines_mod.curr_addr_lines Parameter Value : 10
Info: processor: @5 ns, [PROCESSOR addr_lines_post_wr_cb] : Parameter Name : processor.memory_block.mem_size Parameter Value : 640
Info: processor: @5 ns, [PROCESSOR fn] : The number of address lines can now address the current memory size
Info: param_cfgr: @10 ns, @ 10 ns
Info: param_cfgr: @10 ns, [CFGR] : Changing the 'mem_size' to 800
Info: processor: @10 ns, [PROCESSOR mem_block_post_wr_cb] : Parameter Name : processor.memory_block.mem_size Parameter Value : 800
Info: processor: @10 ns, [PROCESSOR mem_block_post_wr_cb] : Parameter Name : processor.addr_lines_mod.curr_addr_lines Parameter Value : 10
Info: processor: @10 ns, [PROCESSOR fn] : User may proceed with the present configuration
Info: sc_main: End Simulation.
Notes: <number>