## Slide 1: Ex24_Reset_Param SystemC CCI WG
Trevor Wieman
Intel Corp.
March 2018
Notes: <number>

## Slide 2: Parameter Reset
This example shows the effects of reset, specifically:
  Update of value
  Update of value origin
  Triggering of parameter write callbacks
  Note: a “parameter tracker” uses parameter callbacks to report this information.
Variations in behavior are shown for the following parameter types and configurations:
  Mutable and immutable Note: Mutable parameters can be reset
  With preset values
  Locked

## Slide 3: Example Sequence Diagram
simple_ip
@elab
@t = 10ns
Initialize integer parameters
paramA("paramA", 1, "mutable param without preset value")
, paramB("paramB", 2, "mutable param with preset value")
, paramC("paramC", 3, "mutable locked param")
, paramD("paramD", 4, "immutable param")
config_ip
paramC.lock();
m_broker.set_preset_cci_value("sim_ip.paramB",
cci::cci_value::from_json("10"));
Updating mutable parameters.
m_broker.get_param_handle("sim_ip.paramA")
.set_cci_value(cci::cci_value(100));
m_broker.get_param_handle("sim_ip.paramB") .set_cci_value(cci::cci_value(200));
paramA value origin updated to config_ip.
paramB value origin was already config_ip via the preset value.
Notes: <number>

## Slide 4: Example Sequence Diagram - continued
simple_ip
@t = 40ns
@t = 30ns
Resetting parameters (2nd time).
paramA.reset();
paramB.reset();
paramC.reset(); // no effect since paramC is locked
paramD.reset();
config_ip
Updating preset values.
m_broker.set_preset_cci_value("sim_ip.paramA",
cci::cci_value::from_json("1000"));
m_broker.set_preset_cci_value("sim_ip.paramA",
cci::cci_value::from_json(“2000"));
m_broker.set_preset_cci_value("sim_ip.paramA",
cci::cci_value::from_json(“3000"));
m_broker.set_preset_cci_value("sim_ip.paramA",
cci::cci_value::from_json(“4000"));
Notes: <number>

## Slide 5: Example Sequence Diagram - continued
simple_ip
@t = 40ns
@t = 30ns
Resetting parameters.
paramA.reset();
paramB.reset();
paramC.reset(); // no effect since paramC is locked
paramD.reset();
config_ip
paramA and paramD value origins updated to config_ip.
Unlocking and resetting paramB.
paramC.unlock();
paramC.reset();
paramC.lock();
paramC value origin updated to config_ip where its preset value came from.
Notes: <number>

## Slide 6: Expected Output (ex24_Reset_Param.log)
SystemC Simulation
Info: cfg_ip: @0 s, Setting up sim_ip.paramB's preset value to 10
Info: sim_ip: @0 s, Parameter construction complete.
[PTRK @ 0 s] Tracking sim_ip.paramA
handle originator: sc_main
description: mutable param without preset value
value: 1; is default
value origin: sim_ip
[PTRK @ 0 s] Tracking sim_ip.paramB
handle originator: sc_main
description: mutable param with preset value
value: 10; is preset
value origin: cfg_ip
[PTRK @ 0 s] Tracking sim_ip.paramC
handle originator: sc_main
description: mutable locked param
value: 3; locked; is default
value origin: sim_ip
Notes: <number>

## Slide 7: Expected Output - continued
[PTRK @ 0 s] Tracking sim_ip.paramD
handle originator: sc_main
description: immutable param
value: 4; is default
value origin: sim_ip
Info: sc_main: Begin Simulation.
Info: cfg_ip: @10 ns, Updating mutable parameters.
[PTRK @ 10 ns] sim_ip.paramA value updated:
value: 100
value origin: cfg_ip
[PTRK @ 10 ns] sim_ip.paramB value updated:
value: 200
Info: sim_ip: @20 ns, Resetting parameters.
[PTRK @ 20 ns] sim_ip.paramA value updated:
value: 1; is default
value origin: sim_ip
Notes: <number>

## Slide 8: Expected Output - continued
[PTRK @ 20 ns] sim_ip.paramB value updated:
value: 10; is preset
[PTRK @ 20 ns] sim_ip.paramD value updated:
value: 4; is default
Info: cfg_ip: @30 ns, Updating preset values.
Info: sim_ip: @40 ns, Resetting parameters.
[PTRK @ 40 ns] sim_ip.paramA value updated:
value: 1000; is preset
value origin: cfg_ip
[PTRK @ 40 ns] sim_ip.paramB value updated:
value: 2000; is preset
[PTRK @ 40 ns] sim_ip.paramD value updated:
value: 4000; is preset
value origin: cfg_ip
Info: sim_ip: @50 ns, Unlocking and resetting paramC.
[PTRK @ 50 ns] sim_ip.paramC value updated:
value: 3000; is preset
value origin: cfg_ip
Info: sc_main: End Simulation.
Notes: <number>